## Slide 1: Manifesting
Multi-copy document tracking hazardous waste from leaving generator to reaching offsite TSD.
Required for all hazardous wastes shipped offsite with some exemptions.
Generator’s responsibility to ensure correct and complete information.
Keep manifests for at least 3 years.

## Slide 2
Exemptions
  CESQG wastes
  Waste reclaimed under contractual tolling agreement
    Need to meet qualifications
  Universal wastes (fluorescent lamps, batteries, mercury-containing waste)
  Used oil
  Hazardous wastes exempted from RCRA:
    Scrap metal
    Lead-acid batteries to be reclaimed
  When not shipped on manifests, keep any records, such as receipt, bill of lading, etc. to prove these wastes are shipped to right facilities.
Manifesting
Notes: Waste reclaimed under contractual agreement:
The reclaimer come to pick up the waste, reclaim it at their site, return the reclaimed waste to you
There must be an agreement btw the generator and reclaimer. In agreement, identify the type of waste and the frequency of the shipment
The vehicle used to transport the waste and reclaimed waste between your facility and the reclaimer must be owned and operated by the reclaimer
Keep a copy of the agreement at your facility for at least 3 years after the termination of the agreement

## Slide 3
Manifesting
Manifest Page 1

## Slide 4
Manifesting
Working 24/7
Six most representative codes
Specific information of each waste (optional)
Manifest Page 1
Waste paint related material, 3, UN1263, PG III
X
4
DM
220
G
D001 D035 F003 F005 D007 D005
Waste corrosive liquid, basic, inorganic (sodium hydroxide), 8, UN3266, PG II
X
1
DM
55
G
D002
Unique and preprinted
Mark X if hazardous
Notes: Instruction is on the back of each manifest

## Slide 5
Manifesting
Manifest Page 1, continued
If the entire load is rejected:
Alternate TSD your wastes are shipped to, or your facility (generator)
Any additional manifest used to track rejected waste
Management code for each waste in box 9b
H121
H141
Must receive TSD-signed copy in 60 days.
  45 days: contact TSD;
  60 days: notify DEQ.

## Slide 6
Manifesting
Manifest continuation page
X 05. waste flammable liquid, 3, UN1993, PG II 1 DM 55 G
D001
3
4
Must type in or hand write the # shown on page 1

## Slide 7
05 H061
Manifesting
Manifest continuation page, (continued)