Checklist for Autobody Refinishing Shops

Checklist Instructions:  
This checklist is organized in sections, containing questions on the following areas of your shop’s operation:

- Autobody Rule

  - General information

  - Spray guns

  - Spray booths and prep stations

  - Training

  - Paint removal/stripping

  - Documentation, recordkeeping and reporting

- State Rules

  - Air Pollution/VOCs

  - Waste management

  - Wastewater

- Best Management Practices

  - Pollution prevention

  - Energy efficiency

The questions in the checklist are worded so that answering “Yes” means your shop is likely to be in compliance with requirements and answering “No” means you might have a compliance problem that you should investigate further and correct if needed.

At the end of the checklist, we have included a copy of the Notification of Compliance Status form. The deadline for submitting this form was March 11, 2011. If you have not submitted it already, complete this form and send notification to EPA. Also send a copy to DEQ and retain a copy for your records.

If you have any questions about this checklist or the Notification of Compliance Status form, or would like free, confidential compliance assistance, please contact the Pollution Prevention Program:

Cheryl Dirck

Pollution Prevention Program

(405) 702-9128 or (800) 869-1400

Cheryl.Dirck@deq.ok.gov

Basic Facility Information (Required)

| Facility Name: |  |
| --- | --- |
| Facility Address: |  |
| Facility County: |  |
| Name of Person Completing Form: |  |
| Telephone Number of Person Completing Form: |  |
| Facility Owner/Manager Name: |  |

| General Information | Tips and Help Answering the Questions |
| --- | --- |
| 1. Which of the following categories best describes your role at this shop? (mark all that apply) ___ Owner ___ Manager ___ Technician who applies spray coatings ___ Another role (specify)__________________________________ |  |
| 2. What type of services does your shop provide? (mark all that apply) ___ Auto mechanical repair ___ Salvage yard ___ Autobody shop ___ Car dealership ___ Mobile paint service ___ Car wash ___ Other (explain):_________________________________________ |  |
| 3. When did you begin painting operations at your present facility? _______________ _________ ____________ Month Day Year | You are a new source if initial startup was after September 17, 2007. You are an existing source is startup was before September 17, 2007. The dates by which you must comply with the provisions of the rule are based on whether you are a new or existing source. |
| 4. How many employees and paint technicians (or anyone who may paint) do you have in your shop? ___ # employees (total at shop) ___ # paint technicians | # Employees means total for shop, including owner/manager and office staff # Paint technicians includes spraying primers Count all employees, including part-time workers. |
| 5. Does your shop use – check one in each row: Water-based paints: ___ Only ___ Some ___ None Water-based primers: ___ Only ___ Some ___ None Water-based cleaning solvents: ___ Only ___ Some ___ None | Water-based products are often described as those with VOC (volatile organic compounds) content of less than 2 lb VOC/gal. To determine the VOC content of your paints, primers, and solvents, check the MSDS. The section on physical properties (frequently Section 9) will often list the VOC. You can also ask your supplier if your coatings are considered water-based. |
| 6. Do any of the primers, base coats, clear coats, or other coatings used at your shop contain any of these ingredients or compounds including at least one of these? Note that there are specific target concentrations for each ingredient or compound, which are listed in parentheses. Check all that apply: ___ Cadmium (greater than 0.1% by weight) ___ Chromium (greater than 0.1%) ___ Lead (greater than 0.1%) ___ Manganese (greater than 1%) ___ Nickel (greater than 0.1%) ___ None of the paints and coatings used at my shop contain any of the above ingredients. ___ I do not know if my paints contain these ingredients, but will assume they do and comply with the rule. NOTE: If you can answer “None” above, then you may be eligible to petition EPA for an exemption to the spray painting portion of the Autobody rule (NESHAP 6H). If you submit a petition for exemption to EPA, be sure to also submit a copy to DEQ and retain a copy for your records along with all MSDSs that support your exemption. You may operate as though you have been granted the exemption unless you change your operations or receive notice from EPA or DEQ that your petition has been denied. | These five metals—cadmium, chromium, lead, manganese and nickel—have been identified as Hazardous Air Pollutants, and a goal of the Autobody rule is to reduce emissions of these compounds. Compounds with at least one ingredient can include Lead Chromate, Nickel Chromate, or similar mixtures. Typical uses in autobody paints and coatings: Lead and/or chromate are often found in red, orange, and yellow pigments. Cadmium is often found in blue and green pigments. Primer can contain chromium or lead for corrosion resistance. You can refer to lists prepared by the major paint manufacturers that list their product codes for those paints and coatings that include at least one of these regulated materials on this web page: http://www.smallbiz-enviroweb.org/Compliance/NewRules/PaintStripping.aspx Click on “Paint Manufacturing/Petition for Exemption Resources” and then select the links for the appropriate manufacturer of the paint lines you use. Keep a current file of MSDSs for all the coatings and cleaning solvents used at your shop available on-site. |
| 7. Are you aware of DEQ’s Pollution Prevention Program and its free, confidential, non-regulatory compliance assistance services? ____ Yes ____ No ____ Don’t know ____ I would like more information on how to obtain free, non-regulatory compliance help – please contact me. | The contact information for the Pollution Prevention Program is: Cheryl Dirck Pollution Prevention Program (405) 702-9128 or (800) 869-1400 Cheryl.Dirck@deq.ok.gov |
| 8A. How do you prefer to receive regulatory information? (check all that apply) ___ Mailing/written materials ___ Videos – training or “fact sheets” ___ E-mail messages/documents ___ Web training ___ Web site ___ Facebook/twitter/YouTube ___ On site visit ___ Training sessions/workshops offered by suppliers ___ Training sessions/workshops offered by state assistance program ___ Other (specify:________________________________________) 8B. When do you prefer workshops to be held? ____ During the day ____ After work hours |  |

| Spray Guns | Tips and Help Answering the Questions |
| --- | --- |
| This question applies to all spray guns used in your shop, including those that technicians own and use on site. 9A. Are ALL spray guns at your shop HVLP, HVLP-equivalent, electrostatic, airless, or air- assisted airless? ___ Yes ___ No 9B. If you answered YES, identify which gun(s) are used (check all that apply): ___ HVLP ___ HVLP equivalent ___ Electrostatic ___ Airless ___ Air-assisted airless | The Autobody rule requires that only the spray gun types listed in 8A are used after January 10, 2011. “HVLP” is often stamped on the gun handle or cap. If not, contact your spray gun supplier to verify that the make/model is HVLP or HVLP equivalent, or look at purchase records or manuals. HVLP-equivalent means that you have documentation from the gun manufacturer or supplier that it has been approved by EPA. It is strongly recommended that you remove all non-compliant guns from your shop. Conventional guns are not compliant. A list of HVLP approved or equivalent guns is available at http://www.ildceo.net/NR/rdonlyres/81411D97-87CD-40C1-80D7-F6617639FEAD/0/ILHVLPandequivalentgunlist52010.pdf |
| 10A. Is all paint spray gun cleaning done with a fully enclosed spray gun washer or in a way that does not create a mist of solvent? ___ Yes ___ No 10B. If you answered YES, identify which method(s) are used: ___ Fully enclosed spray gun washer ___ Fully enclosed spray gun washer and occasionally disassemble and clean by hand ___ Flush with solvent (but don’t spray) ___ Disassemble gun and clean by hand or mechanical methods | The Autobody rule requires that only the gun cleaning methods listed in 10A are used after January 10, 2011. If the gun is connected to the air compressor during cleaning and you spray solvent through the gun, it will create a mist, which is not compliant with the rule. Pouring solvent through the gun and letting it run out directly into a waste container would not create a mist, and would be acceptable under the rule. |

| Spray Booths and Prep Stations | Tips and Help Answering the Questions |
| --- | --- |
| Does ALL spray coating (including priming) occur in a spray booth or prep station – never out on the shop floor or outdoors? ___ Yes ___ No | The Autobody rule requires that all spray coating be done within a booth, as outlined in the following questions, after January 10, 2011. |
| 12A. When applying a coating to a whole vehicle, or to a component that is still attached to the vehicle, does it ALWAYS occur in a spray booth or prep station that has 4 walls/curtains and a roof? ___ Yes ___ No 12B. How many spray booths or prep stations with 4 walls/curtains and a roof do you have? ______ | The Autobody rule requires that when all or part of a vehicle is being painted, it must be contained within a four-wall booth after January 10, 2011. To meet the enclosure requirements, side curtains may be used in place of walls. Side curtains are typically installed on tracks, so they can be easily opened and closed. Side curtains need to extend from the floor to the roof without any gaps. |
| 13A. When applying a coating to a component that IS removed from the vehicle, does it ALWAYS occur in a spray booth or prep station that has at least 3 walls/curtains and a roof? ___ Yes ___ No 13B. How many spray booths or prep stations with only 3 walls/curtains and a roof do you have? ______ | The Autobody rule requires that when a part is removed from vehicle to be painted, it must be painted in a booth with at least three walls after January 10, 2011. To meet the enclosure requirements, side curtains may be used in place of walls. Side curtains are typically installed on tracks, so they can be easily opened and closed. Side curtains need to extend from the floor to the roof without any gaps. |
| Is each spray booth and prep station that has 4 walls Ventilated at negative pressure, OR Ventilated at positive pressure with seals on all doors and openings, and an automatic pressure balancing system, and operated at no more than 0.05 inches water gauge positive pressure? ___ Yes ___ No | The Autobody rule requires that all four-wall booths be ventilated as indicated in #14 after January 10, 2011. Negative pressure means that air is drawn into the spray booth or prep station. Maintaining negative pressure requires: sufficient make-up air, proper filtration, and venting. |
| Is each spray booth and prep station that has 3 walls ventilated so that air is drawn into the booth? ___ Yes ___ No ___ Not Applicable – we do not have any spray booths or prep stations with only 3 walls – they all have 4 walls | The Autobody rule requires that all three-wall booths be ventilated as indicated in #15 after January 10, 2011. |
| Do ALL spray booth and prep station exhaust systems have an overspray filter system? ___ Yes ___ No | The Autobody rule requires that all booths be exhausted through either a dry filter system or waterwash booth after January 10, 2011. |
| Are spray booth and prep station exhaust/filter systems ALWAYS used when any spray painting (including priming) is done? ___ Yes ___ No |  |
| Is the filter capture efficiency rating of ALL dry filter systems at least 98 percent? ___ Yes ___ No ___ Not applicable – we have a waterwash booth | Filter efficiency information would typically be found on the filter package or provided by the distributor. If you don’t purchase filters directly, but go through a subcontractor instead, you may need to get in touch with them to get the info. The filter documentation provided on the package, or by your distributor or subcontractor, should identify that the filter has been tested consistent with ASHRAE method 52.1. If you don’t know the filter efficiency or that ASHRAE method 52.1 was used to measure it, you must assume the answer to this question is “No”. |
| 19A. Do you have a procedure to determine when exhaust/filter systems need to be cleaned and maintained? ___ Yes ___ No 19B. If you answered YES, how do you decide to when to change a filter? ___ Set schedule (for example, same time each month) ___ Pressure gauge reading ___ Visual check of filter ___ Other - please specify: ________________________ ______________________________________________ ______________________________________________ | There should always be good air flow within the spray booth/prep station so the exhaust/filter system captures all the paint spray, AND there should never be any paint staining outside the fan. A pressure gauge such as a manometer or magnehelic can be used to measure the pressure difference before and after the exhaust filters. As the filter collects more paint solids, this pressure difference increases. Different styles and brands of paint filters will reach their “change out” reading at varying rates depending on paint types, booth design, operator technique, fan speed, temperature, etc. |

| Training | Tips and Help Answering the Questions |
| --- | --- |
| 20A. Have ALL your paint technicians attended a training specifically designed to cover the requirements of the new EPA auto body rule (known as NESHAP 6H)? ___ Yes ___ No 20B. If you answered YES, did the training contain both hands-on and classroom sessions? ___ Yes ___ No | The Autobody rule requires that all painters receive training as described in the rule prior to January 10, 2011, and receive refresher training every five years after the initial training is complete. Many suppliers provide this training. Contact your supplier to see if they are offering trainings that meet this requirement. Career Technology Centers may have added the Rule training requirements to their curriculum in the past year or two, but do NOT assume recent graduates from a technical college have received the proper training. Review transcripts or obtain class descriptions for the year(s) the employee attended. The intent of the training requirements is to improve each painter’s ability to apply coatings in a more efficient manner. Just having a painter hold a spray gun in their hands at the training will not achieve this goal. The hands-on portion of the training should include: Spray gun selection, set up, and operation, including measuring coating viscosity, selecting the proper fluid tip or nozzle, and achieving the proper spray pattern, air pressure and volume, and fluid delivery rate. Spray technique for different types of coatings to improve transfer efficiency and minimize coating usage and overspray, including, maintaining the correct spray gun distance and angle to the part, using proper banding and overlap, and reducing lead and lag spraying at the beginning and end of each stroke. |
| Did the training cover ALL of the following specific topics? ___ Yes ___ No Spray Gun Selection and Set Up - including a hands-on component: Measuring viscosity Selecting proper fluid nozzle or tip Achieving proper spray pattern Air pressure and volume Fluid delivery rate Spray Gun Use – including a hands-on component – on spray technique to improve transfer efficiency and minimize coating usage and overspray, including: Maintaining the correct spray gun distance and angle to the part Using proper banding and overlap Reducing lead and lag spraying at the beginning and end of each stroke Spray Gun Maintenance – including a hands-on component: cleaning method must eliminate creating any solvent mist Spray Booth and Filter Maintenance - including filter selection and installation Description of requirements in the Autobody rule | To answer YES, the training MUST have covered ALL these elements. If any ONE is missing, it is not complete and should be supplemented to be sure it can be certified as complete. |
| Is the training for ALL technicians up-to-date? ___ Yes ___ No | All new technicians must be trained within 180 days of hire. Current technicians were to be trained by July 7, 2008 for new sources and by January 10, 2011 for existing sources– the compliance deadlines listed in the rule. Existing technicians may use experience or previous training that meets the training criteria listed, but that must be documented and the owner must certify that the training was sufficient to meet the rule. All training received is only good for 5 years and a refresher course must be taken prior to the 5 year anniversary. See the following link for an example training form that you may use to track certifications: http://www.epa.gov/ttn/atw/area/ex_painter_training_cert_form.pdf |
| Paint Removal/Stripping | Tips and Help Answering the Questions |
| Is your shop exempt from the methylene chloride paint stripping requirements in the Autobody rule? ___ This shop is exempt because: We do not use any chemical strippers (only mechanical methods like sanding), or We have verified that the chemical strippers used in the shop do not contain Methylene Chloride. If exempt, skip to Question 28. ___ This shop is not exempt because we use a chemical stripper that contains Methylene Chloride. If not exempt, answer Questions 24-27. | The Autobody rule requires that use of methylene chloride to be minimized as much as possible after January 10, 2011. It is strongly recommended that you remove all chemicals containing methylene chloride from your shop, especially if you do not absolutely need them – they are a hazardous waste and must be disposed properly. Methylene Chloride is also known as di-chloromethane (DCM) or methylene dichloride (identified by CAS no. 75-09-2). Check the container label or the MSDS to verify whether any chemical paint strippers in your shop contain this compound. Some likely brands include: StripRDry, Booth Floor Stripper (both made by CMA Philadelphia); Airplane stripper. |
| Do you have records documenting the amount of paint stripping products containing Methylene Chloride your shop uses each year? ___ Yes ___ No How much product containing Methylene Chloride does your shop use each year? ______ gallons per year Does your shop have a plan to reduce or eliminate the use of Methylene Chloride? ___ Yes ___ No If your shop uses 2,000 pounds (~150 gallons) or more in a year, is your plan written and is it posted in the same location where the Methylene Chloride is used? ___ Yes ___ No ___ Not applicable – we use less than 2,000 pounds per yr | Methylene chloride may be abbreviated MeCl on labels or MSDS for products. Plan must: Evaluate need to remove paint Evaluate each application for alternatives: (non- or low-; blasting; mechanical; thermo) Reduce MeCl stripper exposure to air Minimize evaporation during use Ensure proper storage and disposal techniques |

| Documentation, Recordkeeping and Reporting | Tips and Help Answering the Questions |
| --- | --- |
| 28A. Have you submitted an Initial Notification for the Autobody rule as required? ___ Yes ___ No 28B. If you answered YES, do you have a copy in your files and available for review? ___ Yes ___ No | Here is a link to an example initial notification form: http://www.epa.gov/collisionrepair/pdfs/initialnotification.pdf The Initial Notification was due on January 10, 2010. If you missed this deadline, you should send it in as soon as possible to the following addresses: EPA Region VI Director, Air, Pesticides and Toxics 1445 Ross Avenue Dallas, TX 75202–2733 Oklahoma Department of Environmental Quality Air Quality Division 707 N. Robinson P.O. Box 1677 Oklahoma City, OK 73101-1677 |
| Do you have in your files and available for review the required documentation of the efficiency of the filters used to capture paint overspray? ___ Yes ___ No ___ Not applicable – we have a waterwash booth | Filter efficiency information would typically be found on the filter package or provided by the distributor. If you don’t purchase filters directly, but go through a subcontractor instead, you may need to get in touch with them to get the documents. The filter documentation provided on the package, or by your distributor (or subcontractor) should identify that the filter has been tested consistent with ASHRAE method 52.1. |
| 30A. Do you have records on the training each technician received in your files and available for review? ___ Yes ___ No 30B. If you answered YES to 30A, has the shop owner and/or operator certified that the training each technician took meets the requirements of the Autobody rule? ___ Yes ___ No 30C. If you answered YES to 30A, has the training for each technician occurred within the past 5 years? ___ Yes ___ No | Records on file for each technician should include: Name of technician Certificate of training completion Date(s) of training Location of training Training agenda The owner and/or operator of the shop must certify that the training met the requirements of the Autobody rule (also known as 6H or the NESHAP), and this signed certification should also be kept in the file. |
| 31A. Do you have verification that all your spray guns are HVLP, HVLP-equivalent, electrostatic, airless, or air-assisted airless? ___ Yes ___ No 31B. If YES, please describe the documentation available on the spray guns: ___ “HVLP” is stamped on every gun ___ Documentation for every gun in my shop is in my files and available for review ___ “HVLP” is stamped on some guns and documentation is in my files for all the others | Documentation could include that “HVLP” is stamped on the gun, or you can use purchase records or manuals. If you don’t have documentation for every gun, contact your spray gun supplier to get it. Note that HVLP-equivalent means that you have documentation from the gun manufacturer or supplier that it has been approved by USEPA. It is strongly recommended that you remove all non-compliant guns from your shop. Conventional guns are not compliant. |
| Congratulations on completing these initial sections of the self-certification checklist. You now have compiled the information needed to determine whether your shop meets the requirements of the Autobody rule. If you answered “Yes” to all the “Yes / No” questions above, your shop is in compliance with rule requirements. You should have submitted your Notification of Compliance Status by March 11, 2011 to EPA and ODEQ as indicated on the form. If you have not done so already, you should send it as soon as possible. Make sure to keep a copy for your files! If you answered “No” to any “Yes / No” questions above, make any needed changes and then submit the Notification of Compliance Status as soon as possible. Continue on to the next sections of the checklist to complete your evaluation of your shop operations. | Your shop should have been in compliance with all the requirements of the rule by January 11, 2011. The Notification of Compliance Status should have been submitted by March 11, 2011. If you are uncertain about what changes you need to make, or whether you are currently in compliance with any part of this regulation, please contact the Pollution Prevention Program for help. Contact information is listed on the initial page of this checklist. |

| OK Air Rules | Instructions and Tips |
| --- | --- |
| 1. Do you have an air permit on file from the Oklahoma Department of Environmental Quality (ODEQ) Air Quality Division? ___ Yes ___ No  You may need to apply for a permit. | Contact the Air Quality Division to learn about the air permit options available to auto body refinishing/collision repair shops. Oklahoma Department of Environmental Quality Air Quality Division 707 N. Robinson P.O. Box 1677 Oklahoma City, OK 73101-1677 |

| Waste Management | Instructions and Tips |
| --- | --- |
| The questions contained in this section are not exhaustive. They are meant to provide you with a basic understanding of hazardous waste requirements and whether your shop is in compliance. It is best to contact the Pollution Prevention Program to obtain assistance on whether the hazardous waste generated at your shop is being handled properly. |
| WM 1: Have you looked at all of the wastes your shop generates and determined which ones are considered hazardous wastes? ___ Yes ___ No | Paint and solvent wastes are likely to be hazardous wastes. If you have not sent your paint and solvent waste to have it tested, you must assume it is a hazardous waste. Without actual test results, it is best to assume that all rags, filters, etc. in contact with hazardous materials are also hazardous, and should be counted towards your total waste generation (see next question). You are required to have records showing how you classified your wastes (i.e., hazardous or non-hazardous solid waste, or other terms used in your state). Your records must include a description of how you made your waste determination (MSDS, test results, process knowledge, etc.) and copies of documents should be kept in one file so it is easily available! |
| WM 2A: Do you record the amount of hazardous waste that your business generates? ___ Yes ___ No WM 2B: What is the highest amount your shop generates in a month? __________________ Is the amount in pounds or gallons? ___ pounds ___ gallons | Document each waste stream and the weight of material generated (not shipped) per month for each waste stream, add it all up, and compare it to the 220 pound limit. Do not include liquid industrial waste, used oil, or hazardous waste managed as a universal waste. Wastes that may be managed as a universal (or simply non-hazardous) waste in some states include batteries, fluorescent lights, antifreeze, mercury containing switches, and consumer electronics. In addition to waste paint and solvent, you should also include paint filters, still bottoms, and disposable rags, unless you have documentation that confirms they are not hazardous waste. Maintaining a running log of the amount of waste in a waste container at the beginning of each month an easy way to inventory the volume of waste generated. RULES OF THUMB FOR WASTE MEASUREMENTS: 1 pint = 1 pound 1 gallon = 8 pounds 14 gallons or one quarter of a 55-gallon drum = 110 pounds One 55-gallon drum = 440 pounds |
| WM 3: Does your shop generate NO MORE than 220 pounds (26 gallons) of hazardous waste in its busiest month? ___ Yes – never more than 220 pounds a month ___ No If NO, your shop must comply with additional requirements that are not included in this checklist. Skip questions WM4-WM7 and refer to your state waste rules for hazardous waste requirements or other guidance provided here: | If your shop generates MORE than 220 pounds of hazardous waste in a month the shop is a: Small Quantity Generator (SQG) = 27-270 gal/mo; >220 – 2200 lb/mo Large Quantity Generator (LQG) = >270 gal/mo; >2200 lb/mo SQGs and LQGs have more regulatory requirements than this checklist covers. Refer to P2 Program for more information. |
| Questions WM4, WM5, WM6 and WM7 only apply if your shop generates LESS than 220 pounds (about 26 gallons) of hazardous waste in a month. If your shop generates more, you have additional requirements! |
| WM 4: Are ALL your hazardous wastes stored correctly as outlined below? ___ Yes ___ No To answer YES, you must be able to check off ALL actions required: ___ My shop NEVER stores 2200 pounds or more of hazardous waste at one time (approximately five 55 gallon drums) If your shop EVER stores 2,200 pounds or more of hazardous waste at any time, your shop is a Small Quantity Generator and subject to more regulation than is covered in this checklist. Call the P2 Program for more information. | The following are considered best management practices for a conditionally exempt small quantity generator of hazardous waste and are not a requirement of state or federal environmental regulations: ___All hazardous waste is stored in containers or tanks that are in good condition (i.e., free of severe rusting or apparent structural defects, and not leaking) ___ All hazardous waste is stored in a specified location that has a floor resistant to the waste and is protected from the weather ___ All hazardous waste containers are kept closed unless waste is being added or removed ___ There is sufficient aisle space for a person to walk between containers ___ Incompatible materials [e.g., putting rags/towels into waste paint/solvent drums] are kept in separate containers and stored with space between them “Closed” means that if the containers were tipped, nothing would spill. Funnels are acceptable if they are closed and latched. |
| WM 5: Are ALL your hazardous waste containers properly labeled as outlined below? ___ Yes ___ No For IN shops, no labels are required. You can answer Yes if you do not have labels on your containers. | The following are considered best management practices for a conditionally exempt small quantity generator of hazardous waste and are not a requirement of state or federal environmental regulations: ___ All hazardous waste containers are properly labeled with the words “hazardous waste” ___ All drums are labeled with a clear description of the waste inside ___ All drums are clearly marked with the date that waste was first put in the container ___ All containers have a running log of the amount in the drum a the beginning of each month Hazardous Waste Name of Waste _____________ Hazard ______________________ Example label: |
| WM 6: Are you following the proper disposal methods for each of the wastes you generate? ___ Yes ___ No To answer YES, you must make sure your disposal methods are appropriate based on waste disposal guidance. | Information that explains disposal methods allowed for wastes commonly found in autobody shops that generate less than 220 pounds (26 gallons) of hazardous waste in a month are available at. |
| WM 7: Do you have an employee training program that goes over proper hazardous waste management procedures? ___ Yes ___ No | Training should include: Responding to emergencies Handling empty containers and leaks Proper labeling of containers Handling, collecting, segregating, accumulation |

| Proper disposal methods for autobody shops that generate less than 220 pounds (about 26 gallons) of hazardous waste in a month A waste determination is required if these materials are to be disposed. |
| --- |
|  | Transported by licensed hauler for disposal or recycling | Self-transport to CESQG HW collection site | Burn in space heater | Distill or recycle at the shop | Discharge to sanitary sewer or transported to water treatment plant | Trash dumpster | Other allowed options | Policy Documents and other resources |
| Paint waste, including solvent | allowed | allowed | not allowed | allowed | conditional | Allowed/conditional (if non-hazardous) | Off-site recycling |  |
| Still bottoms | allowed | allowed | not applicable | not applicable | not applicable | Allowed/conditional (if non-hazardous) |  |  |
| Rags | allowed | allowed | not applicable | not applicable | not applicable | Allowed/conditional (if non-hazardous) | Laundering | Management of Contaminated Wipes |
| Paper towels | allowed | allowed | not applicable | not applicable | not applicable | Allowed/conditional (if non-hazardous) |  |  |
| Booth filters | allowed | allowed | not applicable | not applicable | not applicable | Allowed/conditional (if non-hazardous) |  |  |
| Oil filters | allowed | allowed | not applicable | not applicable | not applicable | Allowed if hot drained for 24 hr. | Off-site recycling | Used Oil Filters |
| Used Oil | allowed | allowed | allowed | allowed | conditional | Not allowed | Off-site recycling; mixing with generated hazardous waste. | Used Oil |
| Antifreeze | allowed | allowed | not applicable | allowed | conditional | Allowed if non-hazardous | Off-site recycling |  |
| Fluorescent light bulbs | allowed | allowed | not applicable | not applicable | not applicable | Allowed only if low mercury | Off-site recycling | Universal Waste Rule |
| Electronic waste | allowed | allowed | not applicable | not applicable | not applicable | allowed | Off-site recycling | Directory of Reuse and Recycling Options – |
| Batteries | allowed | allowed | not applicable | not applicable | not applicable | Not allowed; must be recycled | Off-site recycling | Universal Waste Rule |

| Wastewater | Instructions and Tips |
| --- | --- |
| The questions contained in this section are not exhaustive. They are meant to provide you with a basic understanding of wastewater requirements and whether your shop is likely to be in compliance. It is best to contact the P2 Program to obtain assistance on whether the wastewater generated at your shop is being handled properly. |
| WW 1: Do you operate a ‘dry’ shop? ___ Yes – Skip remaining WW questions. ___ No – Answer the remaining questions in the wastewater section. | A dry shop is one where no water is used to rinse cars, parts, equipment, floors, or booths. Only rags/wipes (damp or dry), compressed air, brooms or similar techniques are used to clean vehicles and the shop. |
| WW2. In most cases, the only allowed ways to dispose of waste liquids from an autobody refinishing and repair shop is to send it to the local sanitary sewer, or to a holding tank that is later pumped and delivered to a local treatment plant, both of which may require a permit from DEQ. Directing those liquids to a storm drain, onto the ground, into a ditch, into septic systems, into a surface impoundment/pond, or into unknown outlets are not allowed unless a permit to discharge or a total retention permit is obtained from the DEQ. Are you following only allowed discharge practices for your shop waste liquids? ___ Yes ___ No WW 2A. Which of your waste liquids are discharged to storm drain, onto the ground or into a ditch? Check all that apply. ___ Solvents ___ Oil/grease ___ Car wash ___ Antifreeze ___ None ___ Other: __________________ | Discharging wastewater from facility operations to a ditch, ground, septic system, or storm sewer may be illegal or require a permit or authorization. You must know where all drains discharge. If you do not know for sure, you must assume that you have open floor drains when answering this question. Open floor drains with unknown outlets should not be allowed to empty out into storm drains, a septic system, or onto the ground. Check with your local municipality to find contact information for the local wastewater treatment plant or sewer authority in your area. |
| WW 2B. Which of your waste liquids are discharged to septic system? Check all that apply. ___ Solvents ___ Oil/grease ___ Car wash ___ Antifreeze ___ None ___ Other: __________________ WW 2C. Which of your waste liquids are discharged to an unknown outlet? Check all that apply. ___ Solvents ___ Oil/grease ___ Car wash ___ Antifreeze ___ None ___ Other: __________________ WW 2D. Which of your waste liquids are discharged to sewer (local wastewater treatment plant) or a holding tank whose contents are to be transferred to the treatment plant? Check all that apply. ___ Solvents ___ Oil/grease ___ Car wash ___ Antifreeze ___ None ___ Other: __________________ |  |
| WW 3. If you checked anything besides “NONE” in WW 2A, B or C above, has your shop contacted ODEQ to determine if a permit or other authorization is required for any of those activities? ___ Yes ___ No | Please contact the Pollution Prevention Program. |

Best Management Practices in Pollution Prevention and Energy Efficiency

These practices are all voluntary. This checklist will help you evaluate your shop’s progress toward pollution prevention, and will help us understand which practices are most widely used by auto body shops in the state.

| Pollution Prevention Practices | Instructions and Tips |
| --- | --- |
| PP 1: Please check any of the following actions you have taken to reduce air emissions: a. Air Toxics ___ Keep ALL solvent containers closed to limit evaporation ___ Avoid use of coatings that contain toxic metals (chromium, lead, cadmium, nickel, and manganese) by asking suppliers for alternative formulations? ___ Use Paintless dent repair techniques ___ Avoid use of methylene-chloride based paint strippers ___ Automatic enclosed gun washer ___ Use water-based or low-solvent coatings (primers, basecoats and painting) ___ Use low-VOC solvents or thinners ___ Two-stage solvent use (Wash first with used solvent, then wash with clean solvent. When first wash solvent no longer cleans, replace with second wash solvent, replace second wash solvent with fresh solvent, recycle first wash waste solvent.) ___ Recycle solvents with on-site (or off-site) distiller ___ Have an inventory system (first-in, first-out) in place to prevent products from going out of date? ___ Use computerized paint mixing system to minimize mistakes/over-mixing ___ Use non-solvent based putty/fillers ___ Other (specify) b. Dust/Particulate matter ___ Use a disposable paint cup system to minimize unused paint and emissions ___ Use a ventilated sander or self-contained media plaster to minimize emissions from preparing parts ___ Reusable aerosol or pump spray containers ___ Use Roll-on Primer ___ Other (specify) |  |

| Energy Efficiency Practices | Instructions and Tips |
| --- | --- |
| EE 1: Please check any of the following actions you have taken to minimize energy use in your shop: a. Paint booth area: ___ Paint booth energized only when necessary ___ Booth lights kept clean ___ Filters changed regularly to ensure good airflow (which reduces draw on HVAC motors) ___ Paint booth fan motors have variable speed drives ___ Booth uses heated air recirculation ___ Energy efficient equipment (motors, fans, lighting, spray guns) purchased new or for replacement ___ Booth lighting on timers/motion sensors to reduce energy use ___ Other (specify) b. Shop areas: ___ Installed specialized controls (timers, motion sensors) that turn off or throttle back lights, heat, or equipment when areas are not occupied and/or in use ___ Install programmable thermostat for heating/cooling ___ Installed efficient fluorescent lights (<T-12) ___ Encouraged employees to turn off lights ___ Cleaned light fixture reflectors to increase available light ___ Reduced lighting intensity where acceptable ___ Taken advantage of day-lighting ___ Install dusk to dawn lighting fixtures/equipment ___ Completed an energy audit/aware of monthly electricity/fuel use ___ Insulated building, windows and hot/cold ducts or pipes ___ Regularly check your air compressor system for leaks and repair all leaks found. ___ Regularly check your air compressor to ensure that the pressure setting isn’t higher than it needs to be. ___ Use electric tools like shop-vacs or blow dryers instead of the compressed air system? ___ Energy efficient office products/machines (computers, copiers, etc.); reduce number of machines in use ___ High efficiency furnace; In floor heating ___ Other (specify): | Air compressor tips: Walk along compressor pipes/hoses right after turning off the compressor, and listen for hissing. Keep a record of whether the compressor cycles on and off frequently when not in use. A ¼-inch leak can cost you $2,800 per year. Think about whether the air compressor is properly sized for your foreseeable future needs. Every 2 PSI reduced can save you 1% in electricity usage and cost. Turbines for HVLP or small electric tools for specific purposes like buffing or sanding may be preferred to pneumatic. |

Congratulations! You have reached the end of the checklist and have completed your review of your autobody shop operations.  If you answered “Yes” to all the “Yes / No” questions in the checklist, your shop is complying with the applicable federal and state requirements.  If you answered “No” to any “Yes / No” questions above, you may need to make some changes to comply with the requirements.

Submit the completed checklist to the P2 Program listed. Keep a copy for your files, and take the actions needed to bring your shop into compliance.  For help with questions about complying with the regulations, contact the P2 Program.