## Slide 1: Agenda
Environmental, health, and safety regulatory overview
Waste determination
Container management
Other wastes
Manifests
Employee training
Emergency preparedness and response

## Slide 2: Agenda
Q&A session (RCRA)
Wastewater pretreatment
Pollution prevention
Overview of the small quantity generator self-certification program
Q&A (all presenters)
Wrap up

## Slide 3: Context
RCRA and other environmental and safety laws
ODEQ and EPA
ODEQ and other state agencies In Oklahoma
RCRA and other programs at ODEQ

## Slide 4: Major Environmental and Safety Laws
Resource Conservation and Recovery Act (RCRA)
Occupational Safety and Health Act (OSHA)
Toxic Substances Control Act (TSCA)
Comprehensive Environmental Response, Compensation Liability Act (CERCLA/Superfund)
Safe Drinking Water Act (SDWA)

## Slide 5: Major Environmental and Safety Laws
Federal Insecticide, Fungicide, and Rodenticide Act (FIFRA)
Clean Air Act (CAA)
Clean Water Act (CWA)
Atomic Energy Act (AEA)
Hazardous Materials Transportation Act (HMTA)

## Slide 6: ODEQ and EPA
ODEQ is authorized by EPA to manage the hazardous waste regulatory program in the state of Oklahoma

## Slide 7: ODEQ and Other State Agencies
Oklahoma Corporation Commission
Oklahoma Department of Transportation
Oklahoma Department of Health
Oklahoma Department of Mines
Oklahoma Water Resources Board
Oklahoma Conservation Commission
Oklahoma Department of Wildlife

## Slide 8: RCRA and Other Programs at DEQ
ODEQ Divisions
  Land Protection Division
  Water Quality Division
  Air Quality Division
  Environmental Complaints and Local Services Division
  State Environmental Laboratory Services
  Administrative Services Division

## Slide 9: Programs in the Land Protection Division at ODEQ
Inspection/Permitting
  Hazardous Waste Compliance and Inspection Section
    SQG Self-Certification Program
  Hazardous Waste Permitting and Corrective Action Section
  Radiation Management Section
  Solid Waste Compliance and Inspection Section
  Tire Recycling Program
  Underground Injection Control Unit

## Slide 10: Programs in the Land Protection Division at ODEQ
Cleanup/Remediation
  Brownfields Program
  Land Restoration Section
  Site Cleanup Assistance (SCAP) & Armory Cleanup Program
  Superfund Site Remediation Section
  Tar Creek Section
  Voluntary Cleanup Program

## Slide 11: Programs in the Land Protection Division at ODEQ
Assistance
  Risk Management Section
  Solid Waste Planning and Sustainability Unit
  (SQG Self-Certification Program)

## Slide 12: Waste Determination
Waste determination: Determining if a material meets the definition of a hazardous waste

## Slide 13: Two Types of Hazardous Waste
Characteristic waste
Listed waste

## Slide 14: Hazardous Waste Determination Process
Step 1: Is the material a solid waste?
Step 2: Is the waste excluded?
Step 3: Is the waste a listed waste?
Step 4: Is the waste a characteristic waste?

## Slide 15: Characteristic Hazardous Wastes
Ignitability (D001)
Corrosivity (D002)
Reactivity (D003)
Toxicity (D004-D043)

## Slide 16: Characteristic of Ignitability Applies to:
Liquids
Solids
Ignitable compressed gases
Oxidizers

## Slide 17: Ignitable Liquid
A liquid that has a flash point <140° F (60° C)

## Slide 18: How Do You Know If the Material Is a Liquid?
Knowledge
Paint Filter Liquids Test
Pressure Filtration Technique

## Slide 19: How Is the Flash Point Determined?
A test flame is applied to fumes/vapors given off by the sample
  Pensky-Martens Closed-Cup
  Setaflash Closed-Cup

## Slide 20: Alcohol-Content Exclusion
Aqueous solution
Contains <24% alcohol (by volume)

## Slide 21: How Do You Know if a Liquid Waste Is Aqueous?
It contains at least 50% water (by weight)*

## Slide 22: Ignitable Solid
Material is capable of ignition through:
  Friction
  Moisture absorption
  Spontaneous ignition
Material must burn so vigorously and persistently that it creates a hazard

## Slide 23: Ignitable Compressed Gas
Flammable when in a mixture of 13% or less with air
Has a flammable range with air of more than 12%

## Slide 24: Oxidizer
Material that yields oxygen readily to stimulate the combustion of organic matter
  Nitrates, permanganates, chlorates, and peroxide (organic and inorganic) are examples

## Slide 25: Characteristic of Corrosivity
aqueous waste with a pH <2.0 or > 12.5, acids or bases
liquid waste that corrodes carbon steel at a rate of >0.25 inch (6.35 mm) per year

## Slide 26: How do you know if the Waste Is aqueous?
The material must contain at least 20% free water by volume*
  *The definition of aqueous is different when determining the pH of a waste versus evaluating the applicability of the alcohol-content exclusion (where the alcohol must contain at least 50% water by weight).

## Slide 27: How do you know if the Waste is a liquid?
Exactly the same process used for ignitable wastes:
  Knowledge
  Paint Filter Liquids Test
  Pressure Filtration Technique

## Slide 28: How Do You Know If You Have a Corrosive Solid
TRICK QUESTION:
  There are no corrosive solids at the federal Level

## Slide 29: Characteristic of Reactivity
Normally unstable and readily undergoes violent change without detonating
Reacts violently with water, i.e. elemental sodium or potassium
Forms potentially explosive mixtures with water

## Slide 30: Characteristic of Reactivity
Generates toxic gases, vapors, or fumes in quantities sufficient to present a danger to human health or the environment when mixed with water
Cyanide or sulfide-bearing waste that generates toxic gases, vapors, or fumes in a quantity sufficient to present a danger to human health or the environment when exposed to conditions in which the pH is between 2.0 and 12.5

## Slide 31: Characteristic of Reactivity
Capable of detonation or explosive reaction if subjected to a strong initiating source or if heated under confinement
Is readily capable of detonation or explosive decomposition or reaction at standard temperature and pressure
Forbidden explosive (as defined by DOT)

## Slide 32: Examples of Reactive Wastes
Cyanides
Lithium-containing materials
Sodium containing materials
Sulfides
Aluminum alkyls
Acetyl chloride
Chromic acid
Hypochlorites
perchlorates

## Slide 33: Characteristic of Toxicity
Developed to protect groundwater
Includes:
  8 heavy metals
    arsenic, barium, cadmium, chromium, lead, mercury, selenium, silver
  6 pesticides
  26 solvents or other organic chemicals

## Slide 34: Toxicity Characteristic Leaching Procedure (TCLP)
Designed to simulate acidic conditions found in a municipal landfill
Extraction Procedure (EP) Toxicity Test was used prior to 1990

## Slide 35: TCLP – Things to Keep in Mind
Reproducibility
Cost
Oily wastes and organic liquids

## Slide 36: Alternatives to Using the TCLP
Process knowledge
Total waste analysis
  “20 times rule”
Directly analyze liquid wastes for total concentration of toxic constituents
  Wastes that contain less than 0.5% filterable solids
  The waste is already in liquid form - no extraction is necessary

## Slide 37: Listed Wastes
F-List: Process wastes – not industry specific
K-List: Process wastes – industry specific
P and U-Lists: Discarded unused chemicals

## Slide 38: Hazard Codes
Indicate the basis on which EPA listed a particular waste
  Ignitable waste – (I)
  Corrosive waste – (C)
  Reactive waste – (R)
  Toxicity characteristic waste – (E)
  Acute hazardous waste – (H)
  Toxic waste – (T)

## Slide 39: ICR-Listed Wastes
Wastes That Are listed ONLY because they exhibit the characteristic of ignitability, corrosivity, and/or reactivity
29 wastes meet this description
The ICR listing does not apply if the waste does not exhibit the associated characteristic at the point of generation

## Slide 40: F-Listed Wastes
Spent solvents (F001-F005)
Electroplating and other metal finishing wastes (F006-F019)
Dioxin-containing wastes (F020-F023 and F026-F028)
Chlorinated aliphatic hydrocarbon production wastes (F024 and F025)

## Slide 41: F-Listed Wastes
Wood preserving wastes (F032, F034, and F035)
Petroleum refinery wastewater treatment sludges (F037 and F038)
Multisource leachate (F039)

## Slide 42: Spent Solvents
Used for its solvent properties
Too contaminated for further use (i.e. spent)
Meets a specific before-use concentration

## Slide 43: F001
Halogenated solvents
Used in large-scale industrial degreasing operations
Includes five specific chemicals and one class of compounds

## Slide 44: F001 Solvents
Carbon tetrachloride
Methylene chloride
Tetrachloroethylene (perchloroethylene)
1,1,1-trichloroethane
Trichloroethylene
Chlorinated fluorocarbons

## Slide 45: F002
Halogenated solvents
Used in small-scale degreasing operations
Includes 9 specific chemicals

## Slide 46: F002 Solvents
Chlorobenzene
o-dichlorobenzene
Methylene chloride
Tetrachloroethylene (perchloroethylene)
1,1,1-trichloroethane
1,1,2-trichloroethane
1,1,2-trichloro-1,2,2-trifluoromethane
Trichloroethylene
Trichlorofluoromethane

## Slide 47: What is the Difference Between F001 and F002 Solvents?
Four solvents appear on both lists:
  Methylene chloride
  Tetrachloroethylene (perchloroethylene or “perc”)
  Trichloroethylene
  1,1,1-trichloroethane

## Slide 48: How Do You Know Which Waste Code to Use?
F001: used in large-scale industrial degreasing operations
  cold cleaning
  vapor degreasing (open top or conveyorized)
F002: used in small scale degreasing operations
  equipment maintenance or repair
  dry cleaning

## Slide 49: F003
Non-halogenated solvents
Includes 9 specific chemicals
A waste solvent does not carry the F003 listing if it Is not ignitable
Listed only because of the characteristic of ignitability (I)

## Slide 50: F003 Solvents
Acetone
n-butyl alcohol
Cyclohexanone
Ethyl acetate
Ethyl benzene
Ethyl ether
Methanol
Methyl isobutyl ketone
xylene

## Slide 51: F004
Non-Halogenated solvents
  Cresols
  Cresylic Acid
  Nitrobenzene

## Slide 52: F005
Non-Halogenated Solvents
Includes 8 Specific Chemicals

## Slide 53: F005 Solvents
Benzene
Carbon disulfide
2-ethoxyethanol
Isobutanol
Methyl ethyl ketone
2-nitropropane
Pyridine
toulene

## Slide 54: Points to Remember About F-listed Solvents
How the solvent was used MUST be known before a code can be applied
Solvents used as ingredients are not F-listed waste when discarded

## Slide 55: Mixtures of Spent Solvents
Mixtures of F001, F002, F004, and F005 only
Mixtures Containing F003

## Slide 56: Mixtures of F001, F002, F004, and F005 Solvents Only
A solvent mixture containing 10% or more total F001, F002, F004, and F005 solvents will carry the corresponding codes for solvent contained in the solvent mixture
solvent percentage is:
  based on volume
  calculated prior to use

## Slide 57: Spent Solvent Mixture Example No. 1
The concentration (prior to use) of the solvent:
  20% methylene chloride (F002)
  80% water
The total percentage of listed solvents is 20%
Therefore, the spent solvent is F002

## Slide 58: Spent Solvent Mixture Example No. 2
The concentration (prior to use) of the solvent:
  5% trichloroethylene (F001)
  3% cresols (F004)
  2% methyl ethyl ketone (F005)
  90% water
The total percentage of listed solvents is 10%
Therefore, the spent solvent is F001, F004, F005

## Slide 59: Spent Solvent Mixture Example No. 3
The concentration (prior to use) of the solvent:
  35% toluene (F005)
  1% carbon tetrachloride (F001)
  64% unlisted constituents
The total percentage of listed solvents is 36%
Therefore, the spent solvent is F005, F001

## Slide 60: Mixtures Containing F003 Solvents
Solvent mixture contains ONLY F003 solvents before use
Solvent mixture contains one or more F003 solvents AND 10% or more total F001, F002, F004 and/or F005 before use
Neither of the above scenarios apply

## Slide 61: Spent Solvent Mixture Example No. 4
The concentration (prior to use) of the solvent:
  100% acetone (F003)
Therefore, the spent solvent is F003
The solvent can contain small percentages of chemical impurities and still be F003

## Slide 62: Spent Solvent Mixture Example No. 5
The concentration (prior to use) of the solvent:
  91% xylene (F003)
  9% tetrachloroethylene (F002)
No spent solvent listing applies

## Slide 63: Spent Solvent Mixture Example No. 6
The concentration (prior to use) of the solvent:
  89% xylene (F003)
  9% tetrachloroethylene (F002)
  2% methyl ethyl ketone (F005)
The spent solvent is F003, F002, F005
NOTE: Additional examples of spent solvent mixtures can be found at: http://www.epa.gov/waste/hazard/correctiveaction/curriculum/download/hwid-list.pdf

## Slide 64: Specific Industries that Generate K-Listed Wastes
Wood preservation
Inorganic pigments
Organic chemicals
Inorganic chemicals
Pesticides
Explosives
Petroleum refining

## Slide 65: Specific Industries that Generate K-Listed Wastes
Iron and steel
Primary aluminum
Secondary lead
Veterinary pharmaceuticals
Ink formulation
Coking

## Slide 66: P and U-listed Wastes
Unused:
  Commercial chemical products
  Off-specification species
  Container residues
  Spilled product
The P and U list includes unused pharmaceuticals

## Slide 67: P and U-listed Wastes
All P-listed wastes are “acutely” hazardous
Most U-listed wastes are toxic (nonacute)
Some U-listed wastes are listed because they exhibit the characteristic of ignitability (I), Corrosivity (C), or Reactivity (R)
  ICR wastes

## Slide 68: REVIEW: Hazardous Waste Determination Process
Step 1: Is the material a solid waste?
Step 2: Is the waste excluded?
Step 3: Is the waste a listed waste?
Step 4: Is the waste a characteristic waste?
  Remember to perform these steps IN ORDER!

## Slide 69: Generator Categories
Conditionally Exempt Small Quantity Generator (CESQG)
Small Quantity Generator (SQG)
Large Quantity Generator (LQG)

## Slide 70: Small Quantity Generator
Generates between 220 and 2,200 lbs. (100 and 1,000 kg, respectively) of non-acute hazardous waste in a calendar month
Generates no more than 2.2 lbs. (1 kg) of acute hazardous waste per calendar month
Generates no more than 220 lbs. (100 kg) of acute spill cleanup residue per calendar month
Onsite storage of hazardous waste does not exceed 13,227 lbs. (6,000 kg) at any one time